## Slide 1: Quick Guide GV-Data Capture box v3e w/ pcAmerica Resturant POS

## Slide 3
Access the underside of the POS monitor or back of PC:
Attach standard serial cable (RS-232) to available COM port.
Opposite end of cable plugs into GV-Data Capture Box v3e
Note:
Recommend running Hyperterminal test first with Null Modem Cable

## Slide 4
Thermal Printer:
Double check the dip switch positions are in the correct position
  Connection Type
  Baud Rate
Note:
I would recommend to set the serial baud rate to either 19200bps or 9600bps, so that the text overlay don’t scroll to fast on the screen

## Slide 5
GV-Data Capture Box v3e
Front:
Side:
Back:
Change dip switch position of SW1,SW2, and SW3 to match the type of cable used
Attach serial cable (RS-232) to the GV-Data Capture Box v3e and opposite side to the thermal printer
Turn the switch to the correct number that matches the baud rate
Also plug RJ45 cable into the switch

## Slide 6
Device Manager:
Expand > Ports (COM & LPT)
Right click: Communications Port (COM#)
click: Properties
Note:
Serial cable attachment to the COM#
Usually located at the back of the POS or under the monitor
Click: Port settings (tab)
Bits per second: 9600
Note:
The “Bits per second” need to be identical to the GV-Data Capture Box v3e (SW4) and thermal receipt printer
POS:

## Slide 7
Click Start > Devices and Printers
  Click: Add a printer
Add Printer:
Click > Add a local printer
Add Printer:
Select: Use an existing port:
Click and select: Com#: (Serial Port)
Note:
Matching Device Manager and POS COM#

## Slide 8
Add Printer:
Select option below
Manufacturer: Generic
Printers: Generic / Text Only
Click “Next” till “Finish”
Note:
If data capture box already added to DVR/NVR, then you can “Print a test page” that should print to receipt printer and DVR/NVR

## Slide 9
Note:
Recommend “Set as default printer”, if not already defaulted

## Slide 10
POS Application: Restaurants Pro Express
Enter Cashier ID/PW
Note:
Default - 01/admin

## Slide 11
Restaurants Pro Express:
Click on Options
Setup
Friendly Printer Setup

## Slide 12
Printer Setup:
Select printer type:
Either Default or Generic / Text Only
Save & Exit

## Slide 13
DVR/NVR side:
Network and Sharing Center:
Right click: Local Area Connection
  Properties
Select: Internet Protocol Version 4
  Properties
Internet Protocol Version 4 Prop.
IP: 192.168.0.50
Subnet Mask: 255.255.255.0
Default Gateway: 192.168.0.1
Preferred DNS: 192.168.0.1
or
Customer network scheme
Note: Data Capture box default IP address is 192.168.0.100

## Slide 14
Change the network information to fit customer’s network scheme
Click submit

## Slide 18
POS Application: Restaurant Pro express
Test a transaction:
Select:
Any table
Any Party size
Any Food
Click on Pay

## Slide 19
Select
Cash (whole amount)
Popup screen showing change available
Press “OK”
Transaction
Receipt thermal printer
DVR/NVR side (live image)
(watch video)
Video:
Forgot to choose different text color, white hard to see.